## Slide 1: Nuclear Fusion – Is it just a dream?
David Guszejnov

## Slide 2: Why Fusion?

## Slide 3: World Energy Roadmap
By 2050 current consumption will double
IPCC: Only way to avoid climate disaster is to massively invest in low carbon energy sources (renewables and nuclear)

## Slide 4: World Energy Roadmap
Low carbon sources

## Slide 5: Basic Concept of Nuclear Energy
Fission
Fusion

## Slide 6: The Promise of Nuclear Fusion
Advantages:
  Abundant
D + T → 4He(3.52 MeV) + n(14.1 MeV)
From seawater
Unstable! Let’s make it ourselves!

## Slide 7: The Promise of Nuclear Fusion
Advantages:
  Abundant
D + T → 4He(3.52 MeV) + n(14.1 MeV)

## Slide 8: The Promise of Nuclear Fusion
Advantages:
  Abundant Fuel from seawater and Li
  Clean No CO2 or no long-lived radioactive waste

## Slide 9: The Promise of Nuclear Fusion
Advantages:
  Abundant
  Clean
  Safe

## Slide 10: The Promise of Nuclear Fusion
Advantages:
  Abundant Fuel from seawater and Li
  Clean No CO2 or no long-lived radioactive waste
  Safe Negative feedback loop, not weaponizable
Disadvantages:
  Does not work (yet!)

## Slide 11: Realizing Fusion on Earth

## Slide 12: Temperatures
Problem:
Nuclei repel each other, high temperature needed to get them close enough to fuse
T ≈ 66 keV ≈ 100 MK
(All known solids melt above 5000 K)
Fully ionized plasma
What are we going to out this in?
Strong interaction can only counter Coulomb on small scales

## Slide 13: Question of Confinement
We need to hold the plasma together
Ideas:
  Gravity

## Slide 14: Question of Confinement
We need to hold the plasma together
Ideas:
  Gravity
  Inertia
Lasers heat up a solid fuel pellet, the evaporating surface compresses the pellet until it the core ignites
Issue: needs high power, accurate, short burst lasers firing at high frequency

## Slide 15: Inertial Confinement
Lasers heat up a solid fuel pellet, the evaporating surface compresses the pellet until it the core ignites
Issue: needs high power, accurate, short burst lasers firing at high frequency

## Slide 16: Question of Confinement
Charged particles travel along magnetic fields
We need to hold the plasma together
Ideas:
  Gravity
  Inertia
  Magnetic fields
Escapes at the end? Not if there isn’t one.
Honorable mention: Pinch effect
So use a torus and everything is fine, right?

## Slide 17: Magnetic Confinement in a Torus
Torus inner radius smaller inhomogenous B field
Rinner
Router
Idea:
Make particles spend equal amount of time at all radii
Need to „twist” the magnetic field

## Slide 18: Magnetic Confinement in a Torus
Tokamak
Stellarator
(1) vacuum chamber, (2) magnetic coils, (3) plasma, (4) Plasma current, (5) magnetic field, (6) magnetic axis, (7) radial direction, (8) toroidal direction, (9) poloidal direction

## Slide 19: Tokamak

## Slide 20: Brief History
Tokamak (Toroidal Chamber with Magnetic Coils), the most popular fusion reactor design
Invented in 50’s by Tamm and Sakharov
Late 60’s, UK science cooperation, world learns that tokamaks have superior plasma properties compared to all other device types
„Tokamak stampede” in 70’s, oil crisis led to giant investments in fusion, largest device (JET - Joint European Torus) built.
80’s oil prices got low, funding dried up
From the 90’s almost all funding has been invested into ITER, the first experimental fusion reactor, opens in 2025 (actually starts science in 2035)

## Slide 21: Inside a tokamak

## Slide 22: Challenges
Plasma Control
Materials
Politics & Economy

## Slide 23: Plasma Control
Plasmas are extremely hard to control:
  Very hot, must not touch anything
  Evolves on ms timescale
  Prone to dozens of exotic MHD instabilites
Added complications:
  Internal energy generation (fusion), and external „hetaing”
  Radioactive
  Pellet injections to „feed” the plasma
  Failure can destroy the device (but only that, it is not Chernobyl)

## Slide 24: Plasma Instabilities
Many instabilities, here we focus on Edge Localized Modes (ELMs)
  Transport barrier at plasma edge breaks down periodically
  Large amount of heat and material deposited on walls
  May cause plasma disruption

## Slide 25: Runaway electrons
In plasmas dynamic friction may decrease with energy, leading to an avalanche of high energy (MeV) particles

## Slide 26: Runaway electrons
Can happen during plasma diruptions, the runaway electrons often create a self focusing beam that damages or even punctures the vacuum vessel

## Slide 27: Material challenges
Fusion reactor environment
  High magnetic fields (10 Tesla)
  Average heat load of few MW/m2 on walls
  Wall periodicly hit by extreme heat load (few GW/m2)
  Wall ablated by MeV particles
  Extreme neutron flux
  Extraction of radioactive Tritium from „breeder blanket”
  „Affordable” 

## Slide 28: Material challenges

## Slide 29: Politics and Economy
Nuclear fusion research has been chronically underfunded since the 80’s. But there are signs of renewed interest, both in public and private sector.

## Slide 30: The ITER Project

## Slide 31: ITER – The Way
Experimental fusion reactor in France
„iter” means „the way” in Latin (originaly Internation Thermonuclea Experimental Reactor)
International collaboration (EU, US, Russia, India, China, Japan S Korea)
Conceived in late 80’s, building started in 2009 to be finished in 2025
Cost (est.): 20 – 30 billion USD (about NASA’s budget or one new US aircraft carrier)
Aims (after 2025, after 2035):
  Maintain and control >8 min plasma pulses
  Peak Q>10 efficiency, steady state Q>5 (Q>3 needed to break even in power generation)
  Develop Tritium breeding
  Test neutron shield/heat energy conversion

## Slide 32: ITER – Current state

## Slide 33: Summary
Nuclear fusion is promises to transform our lives, but we don’t know yet if it is feasible. If it is (will know by 2035), commercial operations will likely start in the 2050’s (i.e., too late for climate action).